## Slide 1: INS SENSOR CALIBRATION USING ML
Raghunandan
DEAIS
Swapna Sc.E
Dr. Yogeshwar Singh

## Slide 2: PROBLEM STATEMENT
Development of a machine learning model to estimate the complete set of INS sensor calibration parameters, including biases, scale factors, and misalignment terms, while accounting for temperature-dependent variations, for accurate modelling and correction of sensor errors, with the objective of reducing calibration time.

## Slide 3: LITERATURE SURVEY
R. Pesti, P. Sarcevic, and A. Odry, “Artificial neural network-based MEMS accelerometer array calibration,” International Journal of Intelligent Robotics and Applications, 2025, doi: 10.1007/s41315-025-00438-2.
N. B. Vavilova, I. A. Vasineva, A. A. Golovan, A. V. Kozlov, I. A. Papusha, and N. A. Parusnikov, "The Calibration Problem in Inertial Navigation," Journal of Mathematical Sciences, vol. 253, no. 6, pp. 839–860, Mar. 2021. doi: 10.1007/s10958-021-05267-9.

## Slide 4: CORE INSIGHTS
Used an artificial neural network (ANN) to calibrate MEMS accelerometer arrays.
Collected training data using a UR robotic arm for precise ground-truth motion generation.
Calibration performed on data from five IMUs arranged as an accelerometer array.
Trained on ten dynamic datasets and tested on four unseen datasets for generalization.
Achieved 18.2 % better accuracy than ellipsoid fitting.
Achieved 23.3 % better accuracy than simple arithmetic averaging.
Demonstrated that combining ANN calibration with multi-sensor data fusion significantly improves measurement accuracy.
Collected training data using a UR robotic arm for precise ground-truth motion generation.

## Slide 5: GENERAL APPROACH
Collect synchronized raw accelerometer readings (X, Y, Z) and temperature data.
Preprocess and align datasets to remove noise and outliers.
Define target calibration parameters (biases, scale factors, misalignment errors) for all axes.
Train a supervised neural network mapping 4 inputs → 12 error parameters. For example, the four inputs can be accel_x, accel_y, accel_z, temp and the 12 outputs can be all error parameters for all three axes
Apply predicted errors to generate calibrated accelerometer outputs.
Validate performance against reference measurements.

## Slide 6: PROGRESS
Checked all datasets
Full Understanding of Feature Set
Studied the process which was used to get the calibrated acceleration values for each x, y, z axis and the equations and steps involved in it to produce the necessary error parameters like bias, scale factor and misalignment for finding the calibrated value
Identifying and Studying Applicable Neural Network Models